## Slide 1: CS224 I/O

## Slide 2: Timers
Timer1 is 16-bit timer
2^16-1 or 65,535
SYSCLK = 40MHz,
Prescalers
  1:1, 1:8, 1:64, and 1:256
  Use T1CONbits.TCKPS=3 for 1:256 scaling
Prescalar: 1:256, with 40MHz, the timer will be reset every 1/40e6 * 256 * 65535 = 0.419s.

## Slide 3: Timer Implementation

## Slide 4: Analog Input and Output
Interface with the real world
Analog-­‐to-­‐digital-­‐converter(ADC)
Digital-­‐to-­‐analog-­‐converter(DAC)

## Slide 5: Analog-to-Digital Conversion
Terminology
analog: continuously valued signal, such as temperature or speed, with infinite possible values in between
digital: discretely valued signal, such as integers, encoded in binary
analog-to-digital converter: ADC, A/D, A2D; converts an analog signal to a digital signal
digital-to-analog converter: DAC, D/A, D2A
An embedded system’s surroundings typically involve many analog signals.

## Slide 6: Analog Signals
Analog signals – directly measurable quantities in terms of some other quantity
Examples:
Thermometer – mercury height rises as temperature rises
Car Speedometer – Needle moves farther right as you accelerate
Stereo – Volume increases as you turn the knob.

## Slide 7: Just what does an A/D converter DO?
Converts analog signals into binary words

## Slide 8: Digital Signals
Digital Signals – have only two states. For digital computers, we refer to binary states, 0 and 1. “1” can be on, “0” can be off.
Examples:
Light switch can be either on or off
Door to a room is either open or closed

## Slide 9: DAC/ADC Characterisc
Resolution
Dynamic range
Sampling rate
Accuracy

## Slide 10: Example ADC
Resolution: N = 12-­‐bit
Range: Vref- to Vref+ = 0-5 V
Sampling fs = 44 KHz
Accuracy: ± 3 least significant bits (lsbs)

## Slide 11: Analog-to-digital converters
proportionality
Vmax = 7.5V
0V
1111
1110
0000
0010
0100
0110
1000
1010
1100
0001
0011
0101
0111
1001
1011
1101
0.5V
1.0V
1.5V
2.0V
2.5V
3.0V
3.5V
4.0V
4.5V
5.0V
5.5V
6.0V
6.5V
7.0V
analog to digital
4
3
2
1
t1
t2
t3
t4
0100
0110
0110
0101
time
analog input (V)
Digital output
digital to analog
4
3
2
1
0100
1000
0110
0101
t1
t2
t3
t4
time
analog output (V)
Digital input
Embedded Systems Design: A Unified Hardware/Software Introduction, (c) 2000 Vahid/Givargis

## Slide 12: Proportional Signals
Simple Equation
Assume minimum voltage of 0 V.
Vmax = maximum voltage of the analog signal
a = analog value
n = number of bits for digital encoding
  2n = number of digital codes
  M = number of steps, either 2n or 2n – 1
d = digital encoding
a / Vmax = d / M
 | Vmax
 | 0 V
 | 1..1 = 2n-1
… | 
 | 0..0 = 0

## Slide 13: Resolution
Let n = 2
M = 2n – 1
3 steps on the digital scale
d0 = 0 = 0b00
dVmax = 3 = 0b11
M = 2n
4 steps on the digital scale
d0 = 0 = 0b00
dVmax - r = 3 = 0b11 (no dVmax )
r, resolution: smallest analog change resulting from changing one bit
 | Vmax
 | 0 V
 | 3=11
 | 2=10
 | 1=01 0=00
r | 
 | 3=11
 | 2=10
 | 1=01 0=00

## Slide 14: Sampling Rate
Frequency at which ADC evaluates analog signal. As we see in the second picture, evaluating the signal more often more accurately depicts the ADC signal.

## Slide 15: Method to reduce aliasing noise
ADC
Sampling
at 40KHz
output code = n
0110001
0100010
0100100
0101011
:
:
:
Input voltage = V
Low
Pass
Filter:
fcorner=20KHz
e.g.
Max freq
=20KHz
Use low pass filter to remove high frequency
before sampling
Freq.
Gain(dB)
0
-3dB cut off

## Slide 16: PIC32 ADC Basics
Conversion: is when the voltage in the sample and hold capacitor is converted into a binary representation usable in software
For PIC32’s, the conversion is done by means of a successive approximation register (SAR)
A successive approximation ADC compares the pins voltage to an internal analog voltage generated by an internal DAC (digital-to-analog converter of course).
The DAC voltage will be incremented until a match is found. When this happens, the 10-bit value used to drive the DAC becomes the 10-bit analog value.

## Slide 17: PIC 32
10-bit ADC built-in
1 million samples/sec (Msps)
Any of 16 analog input pins
  AN0-15
  Shared with digital I/O port RB
Vref+ = VDD (3.3V)
Vref- = GND(0 V)

## Slide 18: Control Registers
AD1CON1-3
  primary control
AD1CHS
  channel select
AD1PCFG
  pin configuration
AD1CSSL
  see data sheet
ADC1BUF0-F
  10-bit conversion result

## Slide 19: Analog Input Example
#include <P32xxxx.h>
void initadc(int channel) {
AD1CHSbits.CHOSA = channel; // select which channel
AD1PCFGCLR = 1 << channel; // configure input pin
AD1CON1bits.ON = 1; // turn ADC on
AD1CON1bits.SAMP = 1; // begin sampling
AD1CON1bits.DONE = 0; // clear DONE flag
}
int readadc(void) {
AD1CON1bits.SAMP = 0; // end sampling, star conversion
while (AD1CON1bits.DONE); // wait until DONE
AD1CON1bits.SAMP = 1; // resume sampling
AD1CON1bits.DONE = 0; // clear DONE flag
return ADC1BUF0; // return result
}
int main(void) {
int sample;
initadc(11);
sample = readadc();
}

## Slide 20
int analogRead(char analogPIN)
{
AD1CHS = analogPIN << 16;
// AD1CHS<16:19> controls which analog pin goes to the ADC
AD1CON1bits.SAMP = 1; // Begin sampling
while( AD1CON1bits.SAMP );
// wait until acquisition is done
while( AD1CON1bits.DONE );
// wait until conversion done
return ADC1BUF0; // result stored in ADC1BUF0
}

## Slide 21: DAC Conversion
No built-in DACs
Some accept N-parallel wires
Some accept serial (such as SPI)
Flexible voltage vs. not
May need an op-amp

## Slide 22: DAC vs. ADC
DAC:
n digital inputs for digital encoding d
analog input for Vmax
analog output a
DAC
Vmax
x0
x1
Xn-1
…
a

## Slide 23: Examples
AD558 8-bit parallel DAC
  analog.com
LTC1257 12‐bit serial DAC
  linear.com
Texas Instruments also makes

## Slide 24: DAC Circuit

## Slide 25: DAC sine and triangle waves
#include <P32xxxx.h>
#include <math.h>
#define NUMPTS 64
int sine[NUMPTS], triangle[NUMPTS];
void initio(int freq) { // 5-605 Hz frequency
TRISD = 0xFF00; // PORT D outputs
SPI2CONbits.ON = 0; // disable to reset state
SPI2BRG = 9; // 1 MHz SPI clock
SPI2CONbits.MSTEN = 1; // enable master mode
SPI2CONbits.CKE = 1; // set clock-to-data timing
SPI2CONbits.MODE16 = 1; // activate 16-bit mode
SPI2CONbits.ON = 1; // turn SPI on
TRISF = 0xFFFE; // make RF0 an output (load and ce)
PORTFbits.RF0 = 1; // set RF0 = 1
PR1 = (20e6/NUMPTS)/freq – 1; // set period register for frequency
T1CONbits.ON = 1; // turn Timer1 on
}

## Slide 26: DAC Cont’d
void initwavetables(void) {
int i;
for (i=0; i<NUMPTS; i++) {
sine[i] = 2047*(sin(2*3.14159*i/NUMPTS) + 1); // 12-bit
if (i<NUMPTS/2) triangle[i] = i*511/NUMPTS; // 8-bit
else triangle[i] = 510 – i*511/NUMPTS;
}
}
void genwaves(void) {
int I;
while(1) {
for (i=0; i<NUMPTS; i++) {
IFSObits.T1IF = 0; // clear timer overflow flag
PORTFbits.RF0 = 1; // disable load while changing
SPI2BUF = sine[i]; // send points to DACs
PORTD = triangles[i];
while(SPI2STATbits.SPIBUSY); // wait until complete
PORTFbits.RF0 = 0; // load new points into DACs
while (IFSObits.T1IF); // wait until time for next
}
}
}

## Slide 27: DAC main
int main(void) {
initio(500);
initwavetables();
genwaves();
}

## Slide 28: Pulse-width Modulation
Analog through digital duty cycle
Example:
  Output from 0 to 3.3V
  25% duty cycle
Use output compare (OC1‐OC5)
Use Timer 2 or 3 also

## Slide 29: PWM
Is a technique for getting analog results with digital means.
Digital control is used to create a square wave, a signal switched between on and off.
This on-off pattern can simulate voltages in between full on (5 Volts) and off (0 Volts) by changing the portion of the time the signal spends on versus the time that the signal spends off.
The duration of "on time" is called the pulse width.
To get varying analog values, you change, or modulate, that pulse width.
If you repeat this on-off pattern fast enough with an LED for example, the result is as if the signal is a steady voltage between 0 and 5v controlling the brightness of the LED.

## Slide 30: PWM

## Slide 31: Output Compare (PIC32)
OCxCON – control register
  OCM bits set to 110 for PWM
  ON bit enabled
  OCTSEL (Timer2 in 16--‐bit by default)
OCxR – see data sheet
OCxRS – sets duty cycle
Timer’s period register (PR) sets period

## Slide 32: Example
78.125 KHz signal on OC1

## Slide 33: Example Code
#include <P32xxx.h>
void genpwm(int dutycycle) {
PR2 = 255;
// set period to 255+1 ticks (78.125 KHz)
OC1RS = dutycycle;
OC1CONbits.OCM = 0b110;
// set OC1 to PWM mode
T2CONbits.ON = 1;
// default mode (20 MHz, 16-bit)
OC1CONbits.ON = 1;
// turn on OC1
}

## Slide 34: Motors
DC motors
  High current
  Powerful driver (H-bridge)
Servo motors
  Not as powerful
  Specific position (not continuous rotation)
Stepper motors
  Rotates by a fixed angle (step)
  Expensive and need a powerful driver

## Slide 35: PWM Example from Book

## Slide 36: Example Code
void setspeed(int dutycycle) {
OC1RS = dutycycle; // set duty cycle between 0 and 100
}
void setmotorleft(int dir) { // dir of 1 = forward, 0 = back
PORTDbits.RD1 = dir; PORTDbits.RD2 = dir;
}
void initmotors(void) {
TRISD = 0xFFE0;
halt();
T2CONbits.TCKPS = 0b111; // prescale by 256 to 78.125 KHz
PR2 = 99; // set period to 99+1 ticks ~781Hz
OC1RS = 0; // start with low H-bridge enable
OC1CONbits.OCM = 0b110; // set output compare to PWM
T2CONbits.ON = 1;
OC1CONbits.ON = 1; // turn on PWM
}
void halt(void) {
PORTDCLR = 0x001E; // turn both motors off
}

## Slide 37: Servo PIC

## Slide 38: Stepper Motor